## Slide 1: Capacity Analysis and Improvement proposals for Secunderabad Station
Department of Civil and Industrial Engineering
Master’s Degree in Transport Systems Engineering
Candidate
Sai Arvind Atluri
1722524
Relator- Prof. Stefano Ricci

## Slide 2: Index
Objective of study
Methodology
Introduction to the case study
Schematic Representation, Muller Figure
Capacity Analysis
Improvement Proposals

## Slide 3: Objective of study
To determine how different factors affect stations capacity by means of a comprehensive analysis of the complex station.
Potthoff method is used for the evaluation of carrying capacity of complex railway nodes.
Train delays play an important role in capacity analysis.
Focused on average delays, average delay per train and the capacity utilization coefficients.
The timetable is of great importance in capacity analysis of structured railway operation.

## Slide 4: Methodology
Four major stages:
  Data collection,
  Layout and geometry of the station and network representation,
  Analysis method,
  Performance measurements.

## Slide 5: Introduction to case study
Indian Railways is the world’s fourth largest railway system. Founded in 19th century, this system serves millions of tourists and locals, every day.
Secunderabad station: located in the southern part of India and is considered for the analysis. It started operations on 9th October 1874.
One of the major junction stations of SCR (South-Central Railway) provided with 10 platforms. Estimated travellers and visitors is around 0.16 million per day.
Currently Secunderabad junction is planned to cater to different kinds of trains such as the following:
  Long distance Intercity, Rajdhani (Connecting the capital states across India);
  Less passenger density intercity train most of which terminate or originate at Secunderabad;
  Special trains (Festive trains);
  MMTS (Multi Modal Transport System) and suburban trains;
  Mail Express trains ( Super Fast and less number of halts)

## Slide 6: Schematic representation of Secunderabad station

## Slide 7
A | 15 |  | 1 | 15
B | 10 |  | 2 | 10
C | 16 |  | 3 | 16
D | 35 |  | 4 | 35
E | 6 |  | 5 | 6
F | 14 |  | 6 | 14
G | 17 |  | 7 | 17
H | No Stopping |  | 8 | 9
I | 9 |  | 9 | 10
J | 10 |  | 10 | 26
K | 26 |  |  | 
Nodes | Traffic flow
Node -1 | 54
Node -2 | 33
Node -3 | 32
Node -4 | 28

## Slide 8: Capacity check procedure

## Slide 9: Capacity analysis of node 1
 | 1-A | 1-B | 1-C | 1-D | A-2 | B-2 | C-2 | D-2
1-A | A | S | S | S | Z | Z | . | .
1-B |  | A | S | S | Z | Z | . | .
1-C |  |  | A | S | X | X | Z | Z
1-D |  |  |  | A | X | X | Z | Z
A-2 |  |  |  |  | A | Z | Z | Z
B-2 |  |  |  |  |  | A | Z | Z
C-2 |  |  |  |  |  |  | A | Z
D-2 |  |  |  |  |  |  |  | A
Path i | 1-A | 1-B | 1-C | 1-D | A-2 | B-2 | C-2 | D-2
N | 8 | 4 | 2 | 32 | 1 | 1 | 4 | 2
nm = | N*N
 | ƩNiNj
nm = | 1
t̅ = | ƩNiNjTij
 | ƩNiNj
t̅ = | 4.94 min
ƩRij
nm
28.12 min
B = | N t̅
 | nm
B = | 266.7441
Ur = | B
 | T
Ur = | 0.185239
average number of trips
total occupation time
regular utilization coefficient
global utilization coefficient
total delay considering simultaneous movements of nm trains
Ut = | B + ƩRij
 | n̅
 | T
Ut = | 0.204764
X – intersection of routes;
A – between a route and itself; Z – converging routes; S – diverging routes D – consecutive following routes;
U – frontal routes.
average occupation time

## Slide 10: Capacity analysis of node 2
From the graph,
 | 1-I | 1-J | 1-K | I-2 | J-2 | K-2
1-I | A | S | S | Z | Z | Z
1-J |  | A | S | X | Z | Z
1-K |  |  | A | X | X | Z
I-2 |  |  |  | A | Z | Z
J-2 |  |  |  |  | A | Z
K-2 |  |  |  |  |  | A
Path i | 1-I | 1-J | 1-K | I-2 | J-2 | K-2
N | 1 | 2 | 2 | 2 | 4 | 22
nm = | N*N
 | ƩNiNj
nm = | 1
t̅ = | ƩNiNjTij
 | ƩNiNj
t̅ = | 3.93 min
ƩRij
nm
6.15 min
B = | N t̅
 | nm
B = | 129.6126
Ur = | B
 | T
Ur = | 0.090009
Ut = | B + ƩRij
 | nm
 | T
Ut = | 0.094281
average number of trips
total delay considering simultaneous movements of n̅ trains
total occupation time
regular utilization coefficient
global utilization coefficient
average occupation time

## Slide 11: Step -1 Utilization coefficient vs. number of movements
In the step 1, an analysis of utilization coefficient vs. number of movements is taken by increasing the number of trains at regular intervals of 32 units
From the graph, utilization coefficient is increasing as the number of movements of the trains is increasing
Total number of movements (N) | Regular utilization coefficient (Ur) | Global utilization coefficient (Ut)
54 | 0.18 | 0.20
86 | 0.27 | 0.31
118 | 0.35 | 0.43
150 | 0.44 | 0.57
182 | 0.53 | 0.71
214 | 0.62 | 0.87
Chart: Number of movements (N)
| 54 | 86 | 118 | 150 | 182 | 214
 | 0.18524 | 0.26863 | 0.35585 | 0.44446 | 0.53372 | 0.62334
 | 0.20476 | 0.31254 | 0.43467 | 0.56871 | 0.71391 | 0.86999

## Slide 12: Step -2 Average delay per train vs number of movements
In step 2, the average delay per train is calculated using the equation ƩRij / N
Where:
Rij is the average delay;
N is the Number of movements.
From the graph, average delay per train is increasing as the number of movements of the trains is increasing.
ƩRij [min] | N [trains] | ƩRij / N [min/train]
28.12 | 54 | 0.52
63.24 | 86 | 0.73
113.50 | 118 | 0.96
178.92 | 150 | 1.19
259.47 | 182 | 1.42
355.17 | 214 | 1.66
Chart: Number of movements (N)
| 54 | 86 | 118 | 150 | 182 | 214
 | 0.52067 | 0.73534 | 0.96191 | 1.1928 | 1.4257 | 1.6597

## Slide 13: Proposals to improve and enhance station functioning
Graph 1 Graph 2
In the hypothesis the maximum total utilization rate is 75.
The corresponding maximum number of movements is 189 (Black line)
Therefore, we conclude that the maximum number of movements the station can manage for node 1 is 189.
From graph 1 we consider the maximum number of movements is 189 and the corresponding average delay per train is 1.48 minutes (Yellow line)
Chart: Number of movements (N)
| 54 | 86 | 118 | 150 | 182 | 214
 | 0.52067 | 0.73534 | 0.96191 | 1.1928 | 1.4257 | 1.6597
 | 1.48 | 1.48 | 0
Chart: Number of movements (N)
| 54 | 86 | 118 | 150 | 182 | 214
 | 0.18524 | 0.26863 | 0.35585 | 0.44446 | 0.53372 | 0.62334
 | 0.20476 | 0.31254 | 0.43467 | 0.56871 | 0.71391 | 0.86999
 | 0.75 | 0.75 | 0

## Slide 14
Thank you!